UPIWIN: A Micro Windowing Framework for Raspberry Pi
Amy G. Bowersox – December 13, 2019
This project for Hackathon 3.3 involves the development of a framework for running self-contained applications in Python on a Raspberry Pi with LCD graphical output and touchscreen input. The ultimate goal is to produce a framework which is flexible enough to serve any number of “appliance” needs, by using different Python scripts over the same native-code substrate, deployed on an inexpensive embedded platform.
The Platform Hardware
The hardware for this platform consists of a Raspberry Pi 3 Model B computer, to which is attached a PiTFT Plus 2.8” capacitive touchscreen (Adafruit product ID 2423). A specialized case and faceplate (Adafruit product ID 3062 equivalent) enclose the assembled computer and display. The entire device can be assembled for approximately $90 as of this writing, exclusive of onboard MicroSD storage.
The Raspberry Pi 3 is a well-known workhorse in the educational and hobbyist community, being based on a Broadcom BCM2837 quad-core ARM processor running at 1.2 GHz, and having 1 Gb of onboard RAM, HDMI video output, and onboard USB, Ethernet, and WiFi. Its mass storage is provided by a MicroSD card, and its standard operating system is the Raspbian distribution of Linux (based on Debian).
The PiTFT Plus screen is backlit and has a resolution of 320x240 pixels with 16-bit color capability (65,536 total colors possible). The display is driven by the Raspberry Pi’s I2C and SPI data busses, as well as by GPIO pins 25 and 24. In addition, the device has four hardware buttons connected to GPIO pins 17, 22, 23, and 27. The backlight intensity is controllable via pulse-width modulation (PWM) on GPIO pin 18, provided a jumper on the PiTFT board is soldered closed. This has been done on the prototype unit.
N.B.: With the PWM channel in use for the backlight control, the Raspberry Pi can no longer use it to play audio out the headphone jack. A separate USB audio interface is required to play audio; one is currently connected to the prototype unit, though it is not yet in use by the UPIWIN code.

Figure 1: The prototype hardware. The attached keyboard and HDMI display are for development purposes, and will not be part of the assembly in actual use.

Figure 2: A closeup of the prototype hardware.
System Architecture
The UPIWIN executable acts as a host for applications, embedding the CPython interpreter (version 3.7) and providing extension modules to be imported and called by the Python application code. In addition, a thread within the executable polls devices for events (currently the touchscreen and the GPIO buttons) and places retrieved events into a system message queue where they can be retrieved by the Python code running on the main thread.

Figure 3: UPIWIN architecture diagram.
Pieces of this architecture were deliberately crafted to resemble that of Windows, and, as such, several references have been invaluable throughout the course of development:
- The Win32 API documentation, available at https://docs.microsoft.com/en-us/windows/win32/api/.
- The Windows 10 Software Development Kit, particularly its include files, to provide references on data types, structures, and constants.
- The sources to ReactOS (http://reactos.org), an open-source reimplementation of a Windows NT-derived operating system.
- Matt Pietrek, Windows Internals: The Implementation of the Windows Operating Environment (Addison-Wesley, 1993), a guide to the internals of Windows circa version 3.1.
- For reference to certain algorithms used in the code, such as Bresenham’s line-drawing algorithm and the Cohen-Sutherland clipping algorithm, I made use of J.D. Foley and A. Van Dam, Fundamentals of Interactive Computer Graphics (Addison-Wesley, 1982). This was actually one of my college textbooks.
Implementation Details
The touch screen has a Linux framebuffer driver, allowing it to be opened as a device file (/dev/fb1) and directly mapped into the process memory. The total screen buffer size is 153,600 bytes. On the input side, the touch screen maps to the HID framework, and raw event data may be read from /dev/input/touchscreen. The UPIWIN input thread coalesces these raw events into single messages.
Support for the GPIO buttons and backlight is provided by Mike McCauley’s bcm2835 library (http://airspayce.com/mikem/bcm2835/). The input thread simply polls the status of the buttons to determine when to send messages. It employs debouncing logic, as releasing a hardware button would otherwise generate spurious activity on occasion.
Text display support is made possible through use of the FreeType library (http://freetype.org), which is capable of rendering most common font formats, such as TrueType, OpenType, Adobe Type 1, and others.
Bitmaps displayed are currently bound into the executable as straight binary bitmap images. These are converted from PNG format at build time by a small utility program, which makes use of libpng (http://libpng.org/pub/png/libpng.html).
Note that the full power of Python is available to scripts running under UPIWIN. If the script needs to access the filesystem or communicate over the network, it can do so directly without involving UPIWIN. It can even create its own threads; however, developers should be mindful that only the “main” thread of the script should access the UPIWIN UI. (If the main message loop must wait for a message, the UPIWIN input system does release the Global Interpreter Lock, allowing non-UI Python threads to run even as the UI thread is blocked waiting for input.)
The Development Process
The code is actually built on the prototype hardware, which means that source code has to be transferred from my workstation (either my main workstation at home or my work laptop), which is accomplished by pushing the code to my personal Git hosting server, and then pulling it onto the prototype for compilation. In the event of compilation errors, this can be tedious, and debugging frequently has to be done by putting log statements into the code and observing the result. (This technique was termed “disco debugging” by a former coworker of mine, because it’s so 70’s.) Of course, development sometimes has to progress in two languages at once, C for the main executable and Python for the scripts it runs.
At home, I initially had an Ethernet cable connected to the prototype. Since we can’t do that at the office, I prepared it to use Wi-Fi. However, I was unable to get it to connect to the CbGuest Wi-Fi, and wound up using my phone as a hotspot to allow the prototype to connect to the Git server.
The Demo Application
As a demonstration, I have written an application that acts as a simple drawing program, allowing drawing of freehand strokes, lines, hollow rectangles, or solid rectangles in seven different colors. The application also allows the last object drawn to be undone, the entire display to be cleared, and the backlight level of the display to be adjusted. The Python code for the application runs to about 277 lines, and it relies on methods and objects from the “upiwin” package to do its work. It uses the device-independent graphics framework for all its drawing, and relies on certain icons “bound” into the executable for its UI. As part of the framework, the main executable displays a “splash screen” for a couple of seconds prior to executing the script; the original one I created has been replaced for the Hackathon with a VMware Carbon Black logo.
(TK: Insert video demo here)
Future Directions
Although this is a worthy proof-of-concept as it stands, there is a lot of work that can still be done. Here are some things on the project’s future “to do” list:
- Text support has not yet been ported to the device-independent graphics framework. This will require extensive consideration of font handling and enumeration, which the FreeType library will assist with part of.
- There are other graphic operations that could be implemented by the device-independent framework.
- Support for multiple windows needs to be added. Obviously, we won’t necessarily have multiple overlapped windows on such a small display, but having popup windows and “child” windows would be desirable to allow implementation of things like messages, controls, and dialogs.
- Support for resource loading needs to go beyond “embed bitmaps into the executable.” The framework should be able to load PNG or other graphic files, and turn them into device bitmaps for use. (The “mkgfx” tool in the buildutils directory of the source already does this in a static fashion, which is how we bind those bitmaps into the executable in the first place.)
- Since one of the envisioned applications for UPIWIN involves media playback, support for the USB sound adapter needs to be added. This will likely involve media playback running in a separate thread and communicating with the Python script via the message queue.
- Eventually, I need to come up with a way of “stripping down” a Raspbian install and setting it up to automagically run UPIWIN on boot with the desired script. This would be used for packaging actual “appliance” applications, which would not require the keyboard or HDMI display to run.
- Endless other small improvements, such as improvements to the logging and configuration of UPIWIN itself.
The existing source code can be browsed at https://erbosoft.com/git/amy/upiwin/. Owing to the license of one of the libraries used, it is distributed under the GPL version 2.